More maths!
The dot product and projections: another way to see it

---
Dot product : projections
A
B
C
widevec {C} = widevec {A} cdot widehat {B}
widehat {B}
Where is the unit vector of
B

---
Lane filter

---
Autonomous mobile robot
See – think – act
Localization
Cognition
Think
See
Act
Real world
environment
Perception
Motion control
THIS IS THE MOST IMPORTANT SLIDE OF THE WEEK!
Autonomous Mobile Robots – R. Siegwart, I. Nourbakhsh, D. Scaramuzza

---
Following lanes – Overview
Camera
line_detector
line_detector
image
segment_list
lane_filter
lane_filter
robot_pose
line_positions
ground_projection
ground_projection
Motion
Control
lane_controller
lane_controller
car_cmd

---
Localization
Data base
Information
Position
Movement
#
Data base: where are the pillars.
I see a pillar
There are 3 places I can see a pillar from
I moved forward
This is where I can be now
I see a pillar again
There are 3 places I can see a pillar from
Therefore I must be here now
Autonomous Mobile Robots – R. Siegwart, I. Nourbakhsh, D. Scaramuzza

---
Lane filter
Predict
Update
With measurements and database
With movement

---
Localization
Data base
Information
Position
Movement
Position of white, red and
yellow lines with respect
to Moose
Distance from lane center: d
Orientation: φ
Applied
Velocities

---
What do we want to estimate?
Distance d
from center of lane
d > 0 : too much on the left
Orientation φ
from straight direction
φ > 0 : looking too much to the left
φ
d

---
Can we be sure?
Do you see anything
interesting on this
picture?

---
Representing belief
p( d, φ )
1.5
0.2
0.1
φ
0
-0.1
-0.2
...
-1.5
-0.15
...
-0.02
0
0.02
0.04
...
0.3
d

---
Representing belief
p( d, φ )
This is a probability map. The sum of all elements is 1.

---
Representing belief
p( d, φ )
We can estimate the current position and orientation by taking
the coordinates of the maximum in the map!

---
Your turn!
-90
φ (°)
0
90
90
90
90
-30
0
30
d (cm)

---
Lane filter
d
φ
Predict
Update
With position of lanes
With applied velocities

---
Predicting
How would you get
φ_new and d_new?
% %varphi_old
the previous orientation estimation
d_old
the previous position estimation
the angular velocity
%omega
v
the linear velocity
%delta t
the time since previous estimation
% %varphi_new ` = ` ?
d_new ` = `?

---
Your turn! Find a way to estimate φ_new and d_new.
% %varphi_old
the previous orientation estimation
d_old
the previous position estimation
the angular velocity
%omega
v
the linear velocity
%delta t
the time since previous estimation
% %varphi_new ` = ` ?
d_new ` = `?

---
Predicting
Angular velocity ω is the derivative of orientation φ!
%omega = {%varphi( t + %delta t ) - %varphi( t ) } over {%delta t} = {%varphi_new - %varphi_old } over {%delta t}
Therefore:
% %varphi_new ` = `%varphi_old` +` %omega cdot %delta t

---
Predicting
Linear velocity v is the derivative of position... in 2 dimensions!
φ
v
d
dold
dnew

---
Predicting
Linear velocity v is the derivative of position... in 2 dimensions!
φ
We need to project v
in the d direction.
v
v_d = v cdot sin( %varphi )
vd
d
dold
dnew
d_new ` = `d_old` +` v_d cdot %delta t
` = `d_old` +` v cdot sin( %varphi_old )cdot %delta t

---
Predicting
Dynamic equations:
% %varphi_new ` = `%varphi_old` +` %omega cdot %delta t
d_new` = `d_old` +` v cdot sin( %varphi_old )cdot %delta t

---
Propagate prediction on belief
% %varphi_new ` = `%varphi_old` +` %omega cdot %delta t
d_new` = `d_old` +` v cdot sin( %varphi_old )cdot %delta t
Move of each point with a
ω·δt in the φ direction
v·sin(φ)·δt in the d direction

---
Your turn!
-90
φ(°)
0
90
0
30
-30
d (cm)
V = 5 m/s ω = -5°/s dt = 1 s
Give me the d and phi coordinates of each possible location after the update

---
Lane filter
d
φ
Predict
Update
With position of lanes
With applied velocities

---
Updating
Idea: combine
  - Our current idea of where we are: the prior
    p( d, φ )
  - The probability of observations m: the likelihood
    p ( m | d, φ )
To get the posterior
p( d, φ | m)

---
Probabilities...
This is Bayes law!
We want this
(posterior)
We can evaluate this
(likelihood)
We have this (prior)
p ( d, %varphi ` mline ` m ) = {p(m ` mline ` d, %varphi) cdot p(d, %varphi)} over {p(m)}
We don’t need this (normalization constant)

---
Probabilities...
We want this
We can compute this
We have this (prior)
p ( d, %varphi ` mline ` m ) = {p(m ` mline ` d, %varphi) cdot p(d, %varphi)} over {p(m)}
We don’t need this because we can normalize:
sum from{d} sum from{%varphi} p ( d, %varphi ` mline ` m ) = 1

---
Probabilities...
How do we compute the likelihood?
p ( d, %varphi ` mline ` m ) = {p(m ` mline ` d, %varphi) cdot p(d, %varphi)} over {p(m)}

---
Computing the likelihood
1) For each line in m, we compute the corresponding d and φ
2) We add +1 in the corresponding square of a new belief map
3) We normalize the new belief map when we have seen all the lines.
p(m ` mline ` d, %varphi)
is computed by voting.

---
What do we want to estimate?
Distance d
from center of lane
d > 0 : too much on the left
Orientation φ
from straight direction
φ > 0 : looking too much to the left
φ
d

---
Computing the likelihood
1) For each line in m, we compute the corresponding d and φ
2) We add +1 in the corresponding square of a new belief map
3) We normalize the new belief map when we have seen all the maps.
Line position
φ
0
x
y
0
d

---
Computing d and φ for each line
1) For each line in m, we compute the corresponding d, φ and L
x
φ
φ
y
Lanewidth/2 - d
Lanewidth/2 + d
L

---
Your turn!
If the line is white, it has to be on the right.
If the line is yellow, it has to be on the left.
If the line is outside the color band, we have to reduce the computed
d by the width of the lane (white or yellow).

---
Your turn!
How to do this?
Draw, think, figure out the maths
and implement it!
In function def generateVote(self,segment), compute d_i, phi_i and l_i.
You have access to:
- segment.points[0].x, segment.points[0].y, segment.points[1].x, segment.points[1].y are the
x and y coordinates of points 0 and 1 of the segment.
- segment.color = segment.WHITE or segment.YELLOW
- self.lanewidth is the width of the lane
- self.linewidth_yellow and self.linewidth_white are the witdths of yellow and white lines

---
Your turn!
In function def generateVote(self,segment), compute d_i, phi_i and l_i.
You have access to:
- segment.points[0].x, segment.points[0].y, segment.points[1].x, segment.points[1].y are the
x and y coordinates of points 0 and 1 of the segment.
- segment.color = segment.WHITE or segment.YELLOW
- self.lanewidth is the width of the lane
- self.linewidth_yellow and self.linewidth_white are the witdths of yellow and white lines
[Speaker Notes: Hints: - compute the unit vector T and the normal N of each segment. - think about the direction of N - N is also the unit vector of d! - compute the projection of point 0 on N - compute the projection of point 1 on N - what does this represent? - Are they supposed to be the same? Yes! Still, just in case, let’s make the average of both. - compute the projection of point 1 on T - compute the projection on point 2 on T - what does this represent? - Let’s make the average. What does it represent? - Compute the arcsin of T[0]. What does this represent? - What do we have now? - Let’s check if white or yellow, and change d accordingly. - Let’s check in inside or outside, and change d accordingly.]

---
Computing the likelihood
1) For each line in m, we compute the corresponding d and φ
2) We add +1 in the corresponding square of a new belief map
3) We normalize the new belief map when we have seen all the maps.
p(m ` mline ` d, %varphi)
is computed by voting.

---
Your turn!
-90
φ(°)
0
90
0
30
-30
d (cm)
1) Pink: 0 White: 1 Light gray: 2 Dark gray: 3 Black: 4
 What values do we have in the belief map after normalizing?

---
Probabilities...
And this (which is the previous belief)
Now we have this
p ( d, %varphi ` mline ` m ) = {p(m ` mline ` d, %varphi) cdot p(d, %varphi)} over {p(m)}
How do we get the new d, φ map?

---
Your turn!
Likelihood
Prior
-90
-90
φ(°)
0
0
90
90
0
30
0
30
-30
-30
What does the posterior belief map look like?