Autonomous mobile robot
See – think – act
Localization
Cognition
Think
See
Act
Real world
environment
Perception
Motion control
THIS IS THE MOST IMPORTANT SLIDE OF THE WEEK!
Autonomous Mobile Robots – R. Siegwart, I. Nourbakhsh, D. Scaramuzza

---
Cognition
Mission
Position
Movement
command
Global map
Forward!

---
Cognition
Mission
Position
Movement
command
Global map
Advance in the
middle of the lane
d, φ
v, ω

---
Cognition
- Goal
  Advance in the middle of the name
- How?
  Velocity v has to be constant
  Angular velocity ω is used to correct
    - φ
    - d

---
Cognition
- Angular velocity ω is used to correct
  - φ
  - d
  If φ = 0 (looking forward) and d > 0 (too much on the left), what should I do?
  If d = 0 (right at the center) and φ < 0 (looking on the right), what should I do?
  If d = 0, φ_1 < 0 and φ_2 < φ_1, would ω_1 > ω_2?

---
Proportional control

---
Proportional control
v_water = k times e
The water flow F is in liters/second. It is the time derivative of the volume V of water
in the tank :
F(t) = V’(t)
The floater position a is in m, and it is the height of the cuboid formed by the water.
As width and depth are constant, a is proportional to V:
a(t) = V(t)/c
Therefore,
F(t) = c x a’(t)

---
Proportional control
v_water = k times e
F(t) = c x a’(t)
The toilet boil uses a proportional control system:
A is the desired position for the floater (tank is full).
The error e is the difference:
e(t) = A - a(t)
And the toilet lets in a flow proportional to e with a constant k_flow:
F(t) = - k_flow x e

---
Another example: temperature control in your car
Objective: keep the car temperature T at T0 = 25°C

---
Adjusting the heater power
Objective: keep the temperature T(t) at 25°C
We can prove that the power W of the heater/air conditionner is proportional to T’(t):
W = c x T’(t)
How much power should we use to keep the car at T0 = 25?
W = k_heater times ( T_0 - T )
Error e

---
Influence of k_heater
W = k_heater times ( T_0 - T )
The people who made this example are crazy!
Canadians, probably.
T0
https://en.wikipedia.org/wiki/PID_controller#/media/File:PID_varyingP.jpg

---
Influence of k_heater
W = k_heater times ( T_0 - T )
The people who made this example are crazy!
Canadians, probably.
All this is very interesting Vincent.
 But... what is the link with Moose?
T0
https://en.wikipedia.org/wiki/PID_controller#/media/File:PID_varyingP.jpg

---
Let’s summarize.
To use proportional control to keep variable a(t) to desired value a0 we need:
  - To be able to control the derivative a’(t)
  - To be able to measure the error between a(t) and a0
Then, we use:
a'( t) = k_a times (a_0 - a(t))
We have to choose ka correctly, so that we change fast enough but not too much.

---
ω and φ
- We know that ω(t) = φ’(t), and we can control ω(t).
- We can measure φ(t) and we know φ0 = 0
  Therefore, we will use:
%omega_%varphi( t) = k_%varphi times (0 - %varphi) = - k_%varphi times %varphi = k_%theta times %varphi

---
φ(t) and d
We know that
d’(t) = vd(t) = v(t) x sin(φ(t))
We set v(t) as constant.
We use an approximation: sin(x) ≈ x when x is small.
Thinking that φ(t) is small, we have:
d’(t) = v(t) x φ(t)
So we would like :
%varphi_d( t) = k_D times (0 - d) = - k_D times d

---
φ(t) and d
We know that
d’(t) = vd(t) = v(t) x sin(φ(t))
We set v(t) as constant.
We use an approximation: sin(x) ≈ x when x is small.
Thinking that φ(t) is small, we have:
d’(t) = v(t) x φ(t)
So we would like :
But, Vincent, we cannot control φ(t)!
%varphi_d( t) = k_D times (0 - d) = - k_D times d

---
But... we cannot control φ(t)

---
But... we cannot control φ(t)
Yes we can!
%omega_d( t) = k_{%varphi, d} times (%varphi_d - %varphi)
%varphi_d( t) = k_D times (0 - d) = - k_D times d
%omega_d( t) = k_{%varphi, d} times (-k_D - d) = k_d times d

---
So, what do we have
%omega_d( t) = k_{%varphi, d} times (-k_D - d) = k_d times d
%omega_%varphi( t) = k_%varphi times (0 - %varphi) = - k_%varphi times %varphi = k_%theta times %varphi
%omega = k_d times d + k_%theta times %varphi

---
That’s it?
%omega = k_d times d + k_%theta times %varphi
Yes, that’s it!
But now, we have to find kd and kθ.

---
Calibrating kd and kθ
%omega = k_d times d + k_%theta times %varphi
Let’s try it!